# Chiller description

- R134a refrigerant

- Two refrigerant circuits

- Able to unload down to 15% of full load

- Semi-hermetic horizontal helical rotary compressor(s)

- One shell and tube evaporator of falling film type

- Electronic expansion valves

- One water inlet connection and one water outlet connection

- One single main power supply for all the chiller

- Microprocessor based control with user interface

- Rated and certified in accordance with Eurovent standards

- Compliant with EC requirements for machinery, electromagnetic and Pressure Equipment Directive or with national legislations.

# Construction characteristics

- Entirely painted – must withstand 500 hours minimum in a salt-spray fog test

- Weatherproof electrical panels

- Entire coil protected for shipment and rigging

# Compressor characteristics

- Semi-hermetic horizontal helical-rotary type

- Direct drive – maximum speed of screw : 3000 RPM at 50 Hz

- Two rotors in the same horizontal plane

- Suction gas-cooled motor

- Oil lubrication by refrigerant pressure differential between HP and LP

- Continuous load control by slide valve actuated by oil pressure

- Star-delta starter

- Integrated oil filter

# Evaporator characteristics

- Shell and tube – Falling film type

- Freeze protection by trace heater

- Grooved pipes water connections for Victaulic couplings

## Condenser

- Aluminium slit fins mechanically bonded to copper tubes

- Circuiting including subcooling

# Fans

- Fan blades in composite material

- Class F, IP55 motor

- Motor with permanently lubricated ball bearings

Refrigerant circuit

- Two refrigerant circuits - with one or two manifolded compressors on each

- Per circuit :

- Liquid line shut-off valve

- Replaceable core filter dryer

- Electronic expansion valve

- Charging valve

- Discharge and oil line check valves

- Full operating charge of R134a refrigerant and oil

# Electrical panel

- Fully mounted and wired in factory

- Weatherproof

- Full opening access doors

- Lockable through-the-door disconnect switch

- One star-delta closed transition starter per compressor fully factory-mounted and wired

- One single main power supply for the complete chiller (power and control)

- Primary and secondary fused control power transformer

# Control system

- Microprocessor based – Proportional and Integral type

- User interface displaying full messages in clear language

- Access to all control and safety parameters through different menus

- Ensures :

- Load control

- Fault detection

- Start-up of compressors and fans

- Diagnostic and supervision

- Takes corrective actions to prevent shutdown due to abnormal high and low pressure and overcurrent

- Possibility of direct interconnection with a building management system using LonTalk™ open communication protocol

# Text boxes

Air-cooled Series R( Helical-Rotary Liquid Chiller

Model RTAC 120 to 400

(400 to 1500 kW – 50 Hz)

## RLC-PRG002-E4

## CG-PRGXXX-E4

Unit
Description