# Chiller description

- R134a refrigerant

- Two refrigerant circuits – Two compressors

- Able to unload down to 15% of full load

- Semi-hermetic horizontal helical-rotary compressor(s)

- One shell and tube evaporator

- Electronic expansion valves

- One water inlet connection and one water outlet connection

- One single main power supply for all the chiller

- Microprocessor based control with user interface

- Rated and certified in accordance with Eurovent standards

- Compliant with EC requirements for machinery, electromagnetic and Pressure Equipment Directive or with national legislations.

# Construction characteristics

- Entirely painted – must withstand 500 hours minimum in a salt-spray fog test

- Weatherproof electrical panels

# Compressor characteristics

- Semi-hermetic horizontal helical-rotary type

- Direct drive – maximum speed of screw : 3000 RPM at 50 Hz

- Two rotors in the same horizontal plane

- Suction gas-cooled motor

- Oil lubrication by refrigerant pressure differential between HP and LP

- Continuous load control by slide valve actuated by oil pressure

- Star-delta starter

- Integrated oil filter

# Evaporator characteristics

- Shell and tube type

- Freeze protection by heat tape

- Flanged  water connections

## Condenser

- Aluminium slit fins mechanically bonded to copper tubes

- Circuiting including subcooling and oil cooler

# Fans

- Fan blades in composite material

- Class F, IP55 motor

- Motor with permanently lubricated ball bearings

Refrigerant circuit

- Two refrigerant circuits, with one compressor on each

- Per circuit :

- Liquid line shut-off valve

- Replaceable core filter dryer

- Electronic expansion valve

- Charging valve

- Discharge and oil line check valves

- Full operating charge of R134a refrigerant and oil

# Electrical panel

- Fully mounted and wired in factory

- Weatherproof

- Full opening access doors

- Lockable through-the-door disconnect switch

- One star-delta closed transition starter per compressor fully factory-mounted and wired

- One single main power supply for the complete chiller (power and control)

- Primary and secondary fused control power transformer

# Control system

- Microprocessor based – Proportional, Integral and Derivative type

- User interface displaying full messages in clear language

- Access to all control and safety parameters through different menus

- Ensures :

- Load control

- Fault detection

- Start-up of compressors and fans

- Diagnostic and supervision

- Takes corrective actions to prevent shutdown due to abnormal high and low pressure and overcurrent

- Possibility of having a remote user interface able to control a group of four units

- Possibility of interconnection with a building management system through means of a communication interface.

# Text boxes

Air-cooled Series R( Helical-Rotary Liquid Chiller

Model RTAD 85 to 180

(250 to 650 kW – 50 Hz)

Literature Order Number 	RLC-PRG003-E4

Date 		09/03

Supersedes                           RLC-PRG003-E4_1002

Stocking Location 	Europe

Trane has a policy of continuous product and product data improvement and reserves the right to change design and specifications without notice..

Société Trane – Société Anonyme au capital de 61 005 000 Euros – Siege Social:1 rue des Amériques – 88190 Golbey – France – Siret 306 050 188-00011 – RSC Epinal B 306 050 188

Numéro d’identification taxe intracommunautaire: FR 83 3060501888

## RLC-PRG003-E4

## CG-PRGXXX-E4

Trane

##### A business of American Standard

Companies

www.trane.com

For more information, contact

your local district office or e-mail us at

comfort@trane.com

Literature Order Number 	RTHD-PRG001-E4

Date 	08/03

New

Stocking Location 	Europe

Trane has a policy of continuous product and product data improvement and reserves the right to change design and specifications without notice..

Société Trane – Société Anonyme au capital de 61 005 000 Euros – Siege Social:1 rue des Amériques – 88190 Golbey – France – Siret 306 050 188-00011 – RSC Epinal B 306 050 188

Numéro d’identification taxe intracommunautaire: FR 83 3060501888

Unit
Description